## Slide 1: Dayananda Sagar College of Engineering
Electronics and Communication Engineering
(Shavige Malleshwara Hills, Kumaraswamy Layout, Bengaluru – 560 078)
Department of
PYTHON Mini-Project
TOPIC: Canonical form Converter (POS-SOP)
NAME
Vishvendra Singh
Saurabh Singh
Sameer Gautam
USN
1DS18EC156
1DS18EC144
1DS18EC143
Faculty In-charge
Dr. Mahesh Kumar N

## Slide 2
Digital electronics is a field of electronics involving the study of digital signal and the engineering of devices that use or produce them. Digital electronic circuits are usually made from large assemblies of logic gates.
Binary logic deals with binary variables that take 2 discrete values (0 and 1), and with logic operations(AND, OR, NOT). The basic syntax of a binary logic function is F(variables) = Expression.
Boolean algebra(developed by George Boole) is the branch of algebra in which the values of the variables are the truth values true and false, usually denoted by 1 and 0, respectively. Boolean expression can primarily be represented in two ways:
INTRODUCTION

## Slide 3: Sum of Product(SOP)
The sum-of-products (SOP) form is a method (or form) of simplifying the Boolean expressions of logic gates.
Product of Sum(POS)
When two or more sum terms are multiplied by a Boolean OR operation.
f(A,B,C) = ABC + A’BC’
Sum
Product terms
f(A,B,C) = (A’+B) . (B+C’)
Product
Sum terms

## Slide 4
In this form, each product term contains all literals. So, these product terms are the min terms. Hence, canonical SOP form is also called as sum of Min terms form.
Canonical SOP form
In this form, each sum term contains all literals. So, these sum terms are the Max terms. Hence, canonical POS form is also called as product of Max terms form.
Canonical POS form

## Slide 5: Example
The canonical sum-of-products form for f is f(a,b,c) = m1 + m2 + m4 + m6 = a’b’c + a’bc’ + ab’c’ + abc’
The canonical product-of-sums form for f is f(a,b,c) = M0 • M3 • M5 • M7 = (a+b+c)•(a+b’+c’)• (a’+b+c’)•(a’+b’+c’).
Truth Table
a | b | c | f | Min terms | Max terms
0 | 0 | 0 | 0 | a’b’c’ | a+b+c
0 | 0 | 1 | 1 | a'b’c | a+b+c’
0 | 1 | 0 | 1 | a’bc’ | a+b’+c
0 | 1 | 1 | 0 | a’bc | a+b’+c’
1 | 0 | 0 | 1 | ab’c’ | a’+b+c
1 | 0 | 1 | 0 | ab’c | a’+b+c’
1 | 1 | 0 | 1 | abc’ | a’+b’+c
1 | 1 | 1 | 0 | abc | a’+b’+c’

## Slide 6: Conversion Between Canonical Forms (SOP to POS)
Replace ∑ with ∏ and replace those j’s that appeared
in the original form with those that do not.
Example: f1(a,b,c) = a’b’c+ a’bc’+ ab’c’ + abc’ = m1 + m2 + m4 + m6 = ∑(1,2,4,6) = ∏(0,3,5,7) = (a+b+c)•(a+b’+c’)•(a’+b+c’)•(a’+b’+c’)
a | b | c | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Truth Table

## Slide 7: Algorithm to Convert Canonical SOP to POS
Assumption: The input SOP expression is standard ie
Canonical SOP. The variables in SOP expression are
Continuous i.e. if expression contains variable A then it
will have variables B, C respectively and each Product
term contains the alphabets n sorted order i.e. ABC
(not like BAC).
INPUT:
f(A,B,C)= A’B’C + A’BC’+ AB’C’ + ABC’
A’B’C
A’BC’
AB’C’
ABC’
TRUTH TABLE:
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 8
Input as Sum of Min terms
Conversion of Min terms to Binary
Binary to decimal and Stored in a List
Conversion of Numbers not present in
the List to Binary
A’B’C + A’BC’+ AB’C’ + ABC
( 001, 010, 100, 111 )
L=[ 1, 2, 4, 7 ]
( 000, 011, 101, 110 )
( 0, 3, 5, 6 )
Replacing 1 by Complement variable and 0 by Uncomplement Variable by using ‘+’ in between.
(A+B+C), (A+B’+C’),
(A’+B+C’), (A’+B’+C)
Output as POS
(A+B+C).(A+B’+C’).(A’+B+C’).(A’+B’+C’)

## Slide 9: Conversion Between Canonical Forms (POS to SOP)
Replace ∏ with ∑ and replace those j’s that appeared
in the original form with those that do not.
Example: f(A,B,C) = (A+B+C).(A+B+C’).(A’+B+C).(A’+B’+C’) =M0•M1•M4•M7 = ∏(0,1,4,7)
= ∑(2,3,5,6) = A’BC’+A’BC+AB’C+ABC’
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
TRUTH TABLE:

## Slide 10: Algorithm to Convert Canonical POS to SOP
Assumption: The input POS expression is standard.
The variables in POS expression are continuous i.e.
if expression contains variable A then it will have
Variables B, C respectively and each Sum term
contains the alphabets in sorted order i.e.
A + B + C (not like B+A+C).
INPUT:
f(A,B,C)= (A+B+C).(A+B+C’).
(A’+B+C).(A’+B’+C’)
(A+B+C)
(A+B+C’)
TRUTH TABLE:
(A’+B+C)
(A’+B’+C’)
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 11
Input as Product of Max terms
Conversion of Max terms to Binary
(0 for uncomplement and 1 for
complement variable)
Binary to decimal and Stored in a List
Conversion of Numbers not present in
the List to Binary
(A+B+C).(A+B+C’).(A’+B+C).(A’+B’+C’)
( 000, 001, 100, 111 )
L=[ 0, 1, 4, 7 ]
( 000, 011, 101, 110 )
( 2, 3, 5, 6 )
Replacing 0 by Complement variable and 1 by Uncomplement Variable by
using ‘+’ in between.
( A’BC’, A’BC, AB’C, ABC’ )
Output as SOP
A’BC’+A’BC+AB’C+ABC’

## Slide 12: Thank You!